## Slide 1: Airplane Flight Controls

## Slide 2: The three primary flight controls control the airplane’s attitude
Ailerons
Elevator
Rudder
Notes: “System approach” to aviation safety
Methods instructors can use to teach students to use practical risk management tools, discuss how to evaluate student decision-making

## Slide 3
Ailerons
Movement
Turning
Adverse yaw
Types
Elevator
Rudder
Control roll about longitudinal axis
Interconnected—operate simultaneously in opposite directions

## Slide 4
Ailerons
Movement
Turning
Adverse yaw
Types
Elevator
Rudder
Yoke to the right
Right aileron deflects upward (left downward)
Downward deflection increases camber and lift (upward deflection decreases lift)
Increased lift on left wing, decreased on right  turn to the right

## Slide 5
Ailerons
Movement
Turning
Adverse yaw
Types
Elevator
Rudder
Horizontal component of lift
  Counteracts centrifugal force

## Slide 6
Ailerons
Movement
Turning
Adverse yaw
Types
Elevator
Rudder
More lift = more drag
Added drag yaws nose to the direction of the raised wing
Use rudder to counteract
  More needed at low airspeed/high angle of attack and with large aileron deflections

## Slide 7
Ailerons
Movement
Turning
Adverse yaw
Types
Elevator
Rudder
Differential ailerons
  One aileron raise more than other lowered
  Increased drag on descending wing
Frise-type ailerons
  Raised aileron pivots on offset hinge
  Leading edge of aileron into airflow creates drag to equalize lowered aileron drag
  More effective at high AOA

## Slide 8
Ailerons
Elevator
Movement
Types
Rudder
Controls pitch about lateral axis

## Slide 9
Ailerons
Elevator
Movement
Types
Rudder
Pull yoke
Elevator (trailing edge) deflects upward
Upward deflection decreases camber and lift  downward aerodynamic force
Tail moves down—nose pitches up

## Slide 10
Ailerons
Elevator
Movement
Types
Rudder
T-tail
  Elevator above downwash effects
  Slow airspeed—elevator less effective without downwash to assist in raising the nose
Stabilator
  Combines horizontal stabilizer and elevator
Anti-servo tabs
  On trailing edge
  Decrease sensitivity
  Move the same direction as the trailing edge
  Provide resistance so that pilot does not overcontrol the airplane

## Slide 11
Ailerons
Elevator
Rudder
Movement
Controls yaw around vertical axis
Operated though cables

## Slide 12
Ailerons
Elevator
Rudder
Movement
Push left pedal
Rudder moves to the left, altering airflow around vertical stabilizer
Creates sideward force—moves the tail to the right, yaws the nose to the left
Effectiveness increases with speed and slipstream
Purpose
  Counteract adverse yaw
  Provide directional control and coordination