## Slide 1: Operation of Flight Systems
Static System Instruments
Gyroscopic Instruments
Turn Indicators
Compass

## Slide 2
Three instruments operate on static system
  Airspeed indicator
  Altimeter
  Vertical speed indicator
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass

## Slide 3
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Pitot tube—mounted on left wing
  Provides ram air pressure
  Heated through heating element (pitot heat rocker arm switch)
Static ports—on sides of fuselage (x2)
  Provide static air pressure
  Alternate static pressure source beneath panel; activated by push/pull knob
  Lower pressure in cabin—momentary rise in airspeed, altitude, and vertical speed

## Slide 4
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Measures/indicates difference between pitot (impact/dynamic) pressure and static pressure.
Static pressure to airspeed case; pitot pressure to diaphragm.

## Slide 5
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Markings
  White arc (flap operating range)
  Green arc (normal operating range)
  Yellow arc (caution range)
  Red line (never exceed speed)

## Slide 6
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Airspeeds
  Indicated airspeed (IAS)
  Calibrated airspeed (CAS)
  Equivalent airspeed (EAS)
  True airspeed (TAS)
  Groundspeed (GS)

## Slide 7
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Measures height of aircraft above a given pressure level. (Kolesman window)
Series of aneroid wafers expand (when climbing) and contract (when descending) in response to the changing static pressure.

## Slide 8
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Altitudes
  Indicated altitude
  True altitude (MSL)
  Absolute altitude (AGL)
  Pressure altitude
  Density altitude
Errors
  “High to low, look out below; low to high, clear the sky.”
  As the airplane enters an area of lower pressure, the altimeter will read lower than actual if setting not adjusted.

## Slide 9
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Static air enters chamber with calibrated leak—moves diaphragm and linkage.
Instantaneous indication of increase/decrease in rate
Rate of change in altitude once stabilized (6-9 seconds)

## Slide 10
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Pitot tube blocked, drain hole open
  Airspeed indicates zero

## Slide 11
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Pitot tube blocked, drain hole blocked
  Airspeed indicator acts like an altimeter

## Slide 12
Static system
Airspeed indicator
Altimeter
Vertical speed indicator
Errors
Gyroscopic instruments
Magnetic compass
Static port blocked, drain hole blocked
  VSI and altimeter freeze
  Airspeed will read lower above blockage altitude; higher below blockage altitude

## Slide 13
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Rigidity in space
  Gyroscope remains in a fixed position in the plane in which it is spinning

## Slide 14
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Rigidity in space
  Gyroscope remains in a fixed position in the plane in which it is spinning
Precession
  Tilting/turning of a gyroscope in response to a deflective force
  Occurs at a point 90° later in the direction of rotation
  Allows the gyroscope to determine rate of turn

## Slide 15
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Electric
Pressure
Vacuum

## Slide 16
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Vacuum system draws stream of air against the rotor vanes
Air stream spins the gyroscope rotor at high speeds

## Slide 17
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Turn-and-slip indicator
  Rate of turn (degrees per second)
  Coordination
Turn coordinator
  Rate of turn
  Rate of roll
  Coordination
Inclinometer
  Depicts yaw
  Gravity forces ball to rest in lowest part of tube

## Slide 18
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Limitations
  Maximum bank 100°
  Maximum pitch 60°
Instantaneous indication of small changes
Adjustment knob

## Slide 19
Static system
Gyroscopic instruments
Principles
Power
Turn indicators
Attitude indicator
Heading indicator
Magnetic compass
Drifts from set position
  Amount of drift depends on instrument condition

## Slide 20
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Two small magnets attached to metal float—align with Earth’s magnetic field
Hardened steel pivot in float’s center rides inside spring-loaded hard glass jewel cup.
  Allows float freedom
  Float buoyancy takes weight off pivot
  Fluid dampens float oscillation
Flexible diaphragm seal to allow for temperature changes
Compensator assembly
Variation cardholder

## Slide 21
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
Magnetic dip error
Oscillation error

## Slide 22
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
  Also known as declination
  Difference between true and magnetic North
Deviation
Magnetic dip error
Oscillation error

## Slide 23
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
  Local magnetic fields cause compass error
  Differ for each heading
  Not affected by geographic location
  Swinging the compass/cardholder
Magnetic dip error
Oscillation error

## Slide 24
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
Magnetic dip error
  Magnets align with magnetic flux lines—near the poles, they dip (tilt) the float
  Dip-compensating weight that dampens the effect of dip causes other errors
  Northerly turning error
  Acceleration error
Oscillation error

## Slide 25
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
Magnetic dip error
  Northerly turning error (UNOS)
  Vertical component of Earth’s magnetic field pulls north-seeking end of magnet toward the Earth
  Turning from the North to the East/West—initially indicates a turn in the opposite direction
  Turning from the South—turns in the same direction at a faster rate
  Acceleration error
Oscillation error

## Slide 26
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
Magnetic dip error
  Northerly turning error
  Acceleration error (ANDS)
  Dip correction weight causes the south-seeking end of the magnet to be heavier
  East/West heading—float is level
  Accelerating—compass indicates a turn to the North
  Decelerating—compass indicates a turn to the South
Oscillation error

## Slide 27
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Variation
Deviation
Magnetic dip error
Oscillation error
  Combination of all errors
  Compass card swings back and forth around heading
  Use average indication between swings

## Slide 28
Static system
Gyroscopic instruments
Magnetic compass
Errors
Vertical card
Easier to read and use
Eliminates some of the errors
When turning from a heading of North, compass lags
When turning from a heading of South, compass leads turn